## Slide 1
智能体搭建信息输入
①Boundary输入
②correlation输入
③Tube&Fin选型
④期望输出表单

## Slide 2
空气侧Boundary，蒸发器冷凝器通用
Inlet air temperature (4)★
Air relative humidity(5) ★
Air flow(6)★
右图为空气侧工况输入，蒸发器冷凝器通用

## Slide 3
冷媒侧Boundary(冷凝器)
如图：蒸发器冷凝器冷媒侧可各选五种工况条件（E&C代表蒸发器冷凝器都适用），
根据客户输入工况信息进行条件和冷媒的选择

## Slide 4
冷媒侧Boundary(冷凝器)
客户输入冷媒侧工况信息
Entering refrigerant temperature (1)★
Entering refrigerant abs. pressure(1) ★
Refrigerant mass flow rate(1)★
模拟软件对应

## Slide 5
冷媒侧Boundary(冷凝器)
客户输入冷媒侧工况信息
Entering refrigerant abs. pressure(1) ★
Refrigerant mass flow rate(1)★
Quality
模拟软件对应

## Slide 6
冷媒侧Boundary(冷凝器)
客户输入冷媒侧工况信息
Entering refrigerant abs. pressure(1) ★
Entering refrigerant temperature (1)★
Leaving refrigerant subcooling (3)★
模拟软件对应

## Slide 7
冷媒侧Boundary(冷凝器)
客户输入冷媒侧工况信息
Condensing temperature(2) ★
SH=InletT-CondT
Refrigerant mass flow rate(1)★
模拟软件对应

## Slide 8
冷媒侧Boundary(冷凝器)
客户输入冷媒侧工况信息
Condensing temperature(2) ★
SH=InletT-CondT
Leaving refrigerant subcooling (3)★
模拟软件对应

## Slide 9
冷媒侧Boundary(蒸发器)
Refrigerant abs. pressure before valve (3)★ | psia
Refrigerant temperature before valve (3)★ | oF
Refrigerant subcooling before valve (3) | oF
Leaving refrigerant abs. pressure (8) ★ | psia
Leaving refrigerant temperature (8) ★ | oF
Expected Heat rejection capacity★ | Btu/h
Refrigerant mass flow rate★ | lbm/h
Expected EER/COP | 
Leaving refrigerant superheat ★ | oF
Refrigerant side pressure drop limit★ | psid
客户输入冷媒侧工况信息
Inlet P=OutletP+Pressure drop
Inlet T=InletP对应冷媒饱和温度

## Slide 10
冷媒侧Boundary(蒸发器)
Refrigerant abs. pressure before valve (3)★ | psia
Refrigerant temperature before valve (3)★ | oF
Refrigerant subcooling before valve (3) | oF
Leaving refrigerant abs. pressure (8) ★ | psia
Leaving refrigerant temperature (8) ★ | oF
Expected Heat rejection capacity★ | Btu/h
Refrigerant mass flow rate★ | lbm/h
Expected EER/COP | 
Leaving refrigerant superheat ★ | oF
Refrigerant side pressure drop limit★ | psid
客户输入冷媒侧工况信息
Inlet P=OutletP+Pressure drop

## Slide 11
冷媒侧Boundary(蒸发器)
Refrigerant abs. pressure before valve (3)★ | psia
Refrigerant temperature before valve (3)★ | oF
Refrigerant subcooling before valve (3) | oF
Leaving refrigerant abs. pressure (8) ★ | psia
Leaving refrigerant temperature (8) ★ | oF
Expected Heat rejection capacity★ | Btu/h
Refrigerant mass flow rate★ | lbm/h
Expected EER/COP | 
Leaving refrigerant superheat ★ | oF
Refrigerant side pressure drop limit★ | psid
客户输入冷媒侧工况信息
Inlet P=OutletP+Pressure drop

## Slide 12
冷媒侧Boundary(蒸发器)
Refrigerant abs. pressure before valve (3)★ | psia
Refrigerant temperature before valve (3)★ | oF
Refrigerant subcooling before valve (3) | oF
Leaving refrigerant abs. pressure (8) ★ | psia
Leaving refrigerant temperature (8) ★ | oF
Expected Heat rejection capacity★ | Btu/h
Refrigerant mass flow rate★ | lbm/h
Expected EER/COP | 
Leaving refrigerant superheat ★ | oF
Refrigerant side pressure drop limit★ | psid
客户输入冷媒侧工况信息

## Slide 13
冷媒侧Boundary(蒸发器)
Refrigerant abs. pressure before valve (3)★ | psia
Refrigerant temperature before valve (3)★ | oF
Refrigerant subcooling before valve (3) | oF
Leaving refrigerant abs. pressure (8) ★ | psia
Leaving refrigerant temperature (8) ★ | oF
Expected Heat rejection capacity★ | Btu/h
Refrigerant mass flow rate★ | lbm/h
Expected EER/COP | 
Leaving refrigerant superheat ★ | oF
Refrigerant side pressure drop limit★ | psid
客户输入冷媒侧工况信息

## Slide 14
关联式（冷凝器）
关联式对应

## Slide 15
关联式（蒸发器）
关联式对应

## Slide 16
客户输入样品尺寸信息
蒸发器
Available Space for the Coil (Please provide coil dwg if possible) |  |  | 
Length (L)★ | in | mm | 600
Header Height (H)★ | in | mm | 600
冷凝器
需根据输入芯体长宽计算扁管翅片个数，注意单位

## Slide 17
期望输出表单
流程示意（风向、
排数、流程数、冷媒流向）
样品尺寸明细
冷媒侧参数
空气侧参数
单位可切换英制、公制
日期

## Slide 18
Thank you!